## Slide 1: Location-based Routing Algorithms in Mobile Ad Hoc Networks
Sachin Leelasena
Supervisor: Dr J.A. Barria
Notes: Before I start, I want you to imagine a scenario. Let’s say you’ve been to Wembley to see your team win a cup final, or you’ve been to a concert watch your favourite artist. You’re making your way to the nearest tube station in a large crowd as you make your way home. But what you don’t know is that the station is closed due to overcrowding. You have no way of checking either since the large number of people in the area have clogged up the cellular networks. So now you have to fight your way through the crowd and find a different way home, which is annoying enough to ruin your day. But what if there was a way to change that?

## Slide 2: Outline
  Introduction
  Performance Metrics
  System Design
  Results
  Conclusions
Notes: In this presentation I’ll give a brief introduction to my project before covering the key aspects of the system design. The results obtained from the system will be discussed along with the conclusions drawn, before finishing with some ideas for further work.

## Slide 3: Introduction
  No fixed routers in a Mobile Ad Hoc Network (MANET)
  Crowd control for local area events
  Identify best routing algorithm
Notes: Wireless networks typically refer to infrastructure networks which have fixed routers. Mobile ad hoc networks don’t have fixed routers and connections are directly between nodes in the network e.g. between 2 smartphones. All nodes in a MANET can move so the links in the network can change dynamically. This dynamic nature presents some challenges but can also be exploited to give better performance. MANETs are less hardware reliant than infrastructure networks so can be used where it may be too expensive to have a permanent network. They can also be used in rescue operations if infrastructure networks have been damaged for example after an earthquake.
The use case investigated in my project is for crowd control as a response to local area events. A local area event in this context is something that causes disruption to transport links e.g. station closure due to overcrowding or road closure. The crowd being controlled is specifically a crowd of people leaving a stadium after an event such as a football match. In situations like this, cellular networks can get ‘clogged up’ and information transfer can be difficult using infrastructure networks. My project investigates the use of a MANET between smartphones carried by people leaving the stadium being used to propagate information about local area events. The aim of my project is to identify the best routing algorithm to use in this proposed network.

## Slide 4: Performance Metrics – Group Transmission Time (GTT)
  Primary performance measure
  Measure of transmission speed
  Time taken for all relevant nodes in the network to receive the message being propagated
  Theoretical minimum exists:

## Slide 5: Performance Metrics – Power Consumption
  Secondary performance measure
  Considered due to the use of mobile devices
  Average Transmission Power Consumption (ATPC)
    Power consumption as a result of transmission
    Average calculated per node in test group
Notes: End ~ 3 min

## Slide 6: System Design – Overview
Notes: I created a simulation environment using MATLAB where the movement of people leaving Wembley Stadium and heading towards nearby transport links was modelled. I then simulated a station closure and investigated the performance of an ad hoc network where the nodes were smartphones of people heading towards the closed station.
This flowchart shows the overall flow of each simulation. The program flow can be broken down into 3 main components: initialisation, a transmission step and a movement step. The initialisation stage occurs once and the transmission and movement stages loop over a defined number of time slices. Each time slice represents 1 second in real time so the simulation works by simulating the environment as a series of 1 second slices. Once the simulation reaches the end, the results are calculated so a performance comparison can take place.
The system was designed to be as modular as possible to allow common elements to be reused between simulations. The main differences between the simulations of the different algorithms are found in the “transmission possible” decision and simulate transmission step.

## Slide 7: System Design – Mobility Model
  Accurately model people leaving a stadium
  Shortest Path Map Based Movement (SPMBM) mobility model
    Graph representing geographical area
    Dijkstra’s algorithm
  Bioinformatics toolbox
Notes: Try and keep to 1 min

## Slide 8: System Design – Mobility Model 2
  Generates position at each time slice
  Some random behaviour
  Path recalculation limitations
Notes: Try and keep to 1 min

## Slide 9: System Design – Routing Algorithms
  4 algorithms implemented and simulated
    Distance Routing Effect for Mobility (DREAM)
    ‘Reactive’
    ‘Reactive Delay’
    Lightweight Mobile Routing (LMR)
  Transmission via Bluetooth Low Energy (BLE)
    Transmission range
    Transmission timings
Notes: Takes approx 1.5 min
End ~ 8 min

## Slide 10: System Design – Distance Routing Effect for Mobility (DREAM)
  Active routing algorithm
  Location Table
  Message Table
  Update messages
Notes: 30 s

## Slide 11: System Design – ‘Reactive’ Algorithm
  Uses flooding to discover routes
  Routes discarded after 1 second
  Variable transmission limit
Notes: 30 s

## Slide 12: System Design – ‘Reactive Delay’ Algorithm
  Modified version of the Reactive algorithm
  Variable route discovery blocking period
Notes: 30 s

## Slide 13: System Design – Lightweight Mobile Routing (LMR)
  Uses flooding to discover routes
  Only maintains single routes to neighbours
  Routes discarded from cache after transmission
  Routes may be invalid due to blocking period
Notes: 30 s
End ~ 10 mins

## Slide 14: Results – Group Transmission Time
Notes: 2 mins

## Slide 15: Results – Power Consumption
Notes: 1 min
End ~ 13 mins

## Slide 16: Conclusions
  Realistic mobility model implemented
  1 active & 3 reactive algorithms implemented
  GTT & power consumption measured
  Reactive algorithm identified as most suitable for dense networks
  Implementation was challenging
  Simulation framework developed
Notes: 2 mins
End ~ 15 mins

## Slide 17: Background
  Routing protocols
    Active
    Reactive
    Hybrid
    Location-based
  Wireless communication technologies
  Mobility models
  Simulation packages
  Evacuation systems
Notes: Discuss route discovery via flooding – mention what flooding is…

## Slide 18: System Design – Routing Algorithms 2
  Object-oriented approach
  Modular design
  Cell array data structure

## Slide 19: Results – DREAM GTT

## Slide 20: Results – DREAM ATPC

## Slide 21: Results – Reactive GTT

## Slide 22: Results – Reactive ATPC

## Slide 23: Results – Reactive Delay GTT

## Slide 24: Results – Reactive Delay ATPC

## Slide 25: Results – LMR GTT

## Slide 26: Results – LMR ATPC

## Slide 27: Results – LMR PTER

## Slide 28: Further Work
  Test different algorithms
  Increase graph complexity
  Increase complexity of local area event
  Move away from MATLAB